## Slide 1: Development of arduino device for Pollution Monitoring

## Slide 2: introduction

## Slide 3: Pollution is a serious concern !!
Oh Really ?

## Slide 4: So, What is Pollution?
Pollution is the introduction of contaminants into the natural environment that cause adverse change.
A pollutant is a substance or energy introduced into the environment that has undesired effects

## Slide 5: Let’s Talk about Our Device

## Slide 6
Pollution
Pollution
Detector
Device

## Slide 7
Polluion
Pollution
Detector
Device

## Slide 8
Pollution
Sensor
Modulate A-signals
Board Device
Display
Data

## Slide 9: Board Device

## Slide 10: Arduino Device
Digital Pins
Analog Pins
Power pins
Microcontroller(ATmega328P)
UIC
USP Port
Tx & Rx Led
DC Power
Voltage Regulator

## Slide 11: Sensor
MQ135 - Air Quality Gas Sensor Module

## Slide 12: MQ Sensors
MQ-2 - Methane, Butane, LPG, smoke
MQ-3 - Alcohol, Ethanol, smoke
MQ-4 - Methane, CNG Gas
MQ-5 - Natural gas, LPG
MQ-6 - LPG, butane gas
MQ-7 - Carbon Monoxide
MQ-8 - Hydrogen Gas
MQ-9 - Carbon Monoxide, flammable gasses
MQ131 - Ozone
MQ135 - Air Quality (CO, Ammonia, Benzene, Alcohol, smoke)
MQ136 - Hydrogen Sulfide gas
MQ137 - Ammonia
MQ138 - Benzene, Toluene, Alcohol, Acetone, Propane, Formaldehyde gas, Hydrogen
MQ214 - Methane, Natural gas
MQ216 - Natural gas, Coal gas

## Slide 13
Anti-explosion network
Clamp ring

## Slide 14
Sensing Elements
Connecting legs

## Slide 15
Sensing Element
Coating of tin dioxide
Aluminum Oxide bases ceramic

## Slide 16: Internal structure of sensing element
Coating of tin dioxide
Aluminum Oxide bases ceramic
Platinum Wires
Nickel-Chromium coil

## Slide 17
How does a gas sensor work?
When tin dioxide (semiconductor particles) is heated in air at high temperature, oxygen is adsorbed on the surface. In clean air, donor electrons in tin dioxide are attracted toward oxygen which is adsorbed on the surface of the sensing material. This prevents electric current flow.
In the presence of reducing gases, the surface density of adsorbed oxygen decreases as it reacts with the reducing gases. Electrons are then released into the tin dioxide, allowing current to flow freely through the sensor.

## Slide 18: Calibration
Sensitivity adjustment

## Slide 19: How we’ll collect Data?
A0
D0
VCC
GND
A0

## Slide 21: Circuit
Buzzer
LCD
MQ135
Arduino
BreadBoard

## Slide 22: Programming
For the sensor:-
#include “MQ135.h”
float MQ135::getPPM() {
return PARA * pow((getResistance()/RZERO), -PARB);
}
//Function used
float MQ135::getResistance() {
int val = analogRead(_pin);
return ((1023./(float)val) * 5. - 1.)*RLOAD;
}

## Slide 23: Understanding “MQ135.h” File
#ifndef MQ135_H
#define MQ135_H
#if ARDUINO >= 100
#include "Arduino.h"
#else
#include "WProgram.h"
#endif
/// The load resistance on the board
#define RLOAD 10.0
/// Calibration resistance at atmospheric CO2 level
#define RZERO 76.63
/// Parameters for calculating ppm of CO2 from sensor resistance
#define PARA 116.6020682
#define PARB 2.769034857
/// Parameters to model temperature and humidity dependence
#define CORA 0.00035
#define CORB 0.02718
#define CORC 1.39538
#define CORD 0.0018

## Slide 24
class MQ135 {
private:
uint8_t _pin;
public:
MQ135(uint8_t pin);
float getCorrectionFactor(float t, float h);
float getResistance();
float getCorrectedResistance(float t, float h);
float getPPM();
float getCorrectedPPM(float t, float h);
float getRZero();
float getCorrectedRZero(float t, float h);
};
#endif
Understanding “MQ135.h” File

## Slide 25: Main Programming
#include "MQ135.h"
#include <SoftwareSerial.h>
#define DEBUG true
const int sensorPin= 0;
int Contrast=80;
int air_quality;
#include <LiquidCrystal.h>
LiquidCrystal lcd(12,11, 5, 4, 3, 2);
void setup() {
pinMode(8, OUTPUT);
analogWrite(6,Contrast);
lcd.begin(16,2);
lcd.setCursor (0,0);
lcd.print ("Pollution Detector ");
lcd.setCursor (0,1);
lcd.print ("Sensor Warming ");
delay(1000);
lcd.clear();
}
Pollution Detector
Sensor Warming

## Slide 26
void loop() {
MQ135 gasSensor = MQ135(A1);
float air_quality = gasSensor.getPPM()*1000;
lcd.setCursor (0, 0);
lcd.print (“Level = );
lcd.print (air_quality);
lcd.print (" PPM ");
lcd.setCursor (0,1);
if (air_quality<=1000)
{
lcd.print("Fresh Air");
digitalWrite(8, LOW);
}
else if( air_quality>=1000 && air_quality<=2000 )
{
lcd.print("Poor Air ");
digitalWrite(8, HIGH );
}
else if (air_quality>=2000 )
{
lcd.print("Danger!!");
digitalWrite(8, HIGH); // turn the LED and Buzzer on
}
delay(1000);
}
}

## Slide 27
Level = 135
Fresh Air
Level = 1100
Poor Air
Level = 2350
Danger !!
LED = on
Buzzer = on
LED = on
Buzzer = on
LED = off
Buzzer = off

## Slide 28: Let’s see demonstration
Video Here

## Slide 29: Thanks to you for listening

## Slide 30: Any Questions ?